## Slide 1
SELECTED PROJECT LANTERNS

## Slide 2
flexible mount system
- high IP
- high IK
- high corrosion an UV resistance
- availability of various mount options
- availability of various finishes
- availability of service/spare parts
- available as „families”
Project lantern
durable diffuser
- efficiency over 90lm/W
- availability of various colour temp.
- availability of various lens types
- modern steering option (DALI, Zhaga)
- high Ta (for selected locations)
- L70B50 >100 000h
- driver durability and longevity
(desired features)
efficient radiator
proper LED light source
ULOR inhibitor

## Slide 3
Asker and Asker Big
LED colour temp. 3000K/4000K
(other colour options on request)
standard version up/down:
- luminous power 8,8W
- luminous flux 312lm
- available in many up-down light output configurations
- high power light output DALI versions
available
- galvanized steel version available
standard version up/down:
- luminous power 8,3W
- luminous flux 547lm

## Slide 5
Notes: Następny slajd (Lilehammer) działa z opóźnienie, trzeba poczekać sekundę.

## Slide 6
equipped with efficient
LED light sources
available in many up-down narrow-wide light output configurations modified by using a set of lens, shutters and covers.
Lillehammer
- IP65
- IK08
- 4W and 7,3W options
- LED colour temp. 3000K/4000K
Notes: Działa z opóźnieniem, trzeba poczekać sekundę (nie wiem czemu)

## Slide 8
Notes: Click – ON; click - OFF

## Slide 9
2 LED modules up-down
wattage 14.6W (per side)
luminous flux 68,5lm (per side)
- IP65
- IK08
- driver durability 100 000h
- L70B50 >70 000h
- DALI
Lysfjord
Art. 6408
Art. 6403

## Slide 11
several heights
wattage 21,9W
luminous flux 1681lm
efficiency 76.8lm/W
- IP65
- IK08
- transparent PMMA lens
- colour temp. 3000K/4000K
- DIM/DALI versions avaliable
wattage 9.1W
luminous flux 864lm
efficiency 94.9lm/W
Egersund
Art. 5068
Art. 1290

## Slide 13
aluminium body
equipped with
LED lens type V
(other lens versions avail.)
- IP65
- IK08
- colour temp. 3000K or 4000K
- luminous flux 604lm
- driver durability 50 000h
- L70B50 over 260 000h
equipped with electric socket E (Uni)
(other socket versions possible)
Skara 2947
Art. 2935
Art. 2947

## Slide 14
durable mount system
- IP65
- IK08
- wattage 7.4W
- luminous flux 703lm
- efficiency 95lm/W
- L70B50 >109 000h
Trysil 1100
aluminium body
equipped with
LED lens type V
(other lens versions avail.)

## Slide 15
Notes: Day/Night – on click.

## Slide 16
service door
for easy access
improved luminous flux 1416lm
(in comparison with classic versions)
- IP65
- IK10 (excellent durability )
- wattage 22.2W
- colour temp. 3000K/4000K
- L70B50 72 000h
- driver durability 100 000h
- power factor PF 0.95
transparent PMMA
diffuser
Narvik 1736

## Slide 18
Namsos 6033
- IP65
- IK07
- wattage 13.8W
- luminous flux 904lm
- efficiency 65.5lm/W
- power factor PF 0,98
- L70/B50 >102 000h
safety satin glass
DALI
aluminium body
robust mount system

## Slide 20
aluminium body
luminous flux 1396lm
- IP65
- IK08
- efficiency 87.8lm/W
- power factor PF 0,99
- driver durability 100 000h
- L70/B50 >72 000h
4 heights as standard
(35; 55; 85 and 110cm)
Borg Bollard
Art. 6193
Art. 6183
Art. 6172
Art. 6122
DALI

## Slide 22
- IP65
- wattage 11,9W
- luminous flux 1537lm
- efficiency 129,2lm/W
- L70/B50 > 100 000h
Hellvik
DALI
Art. 2416
Art. 2406
durable mount system
equipped with
LED lens type V (CHECK)
(other lens versions available)

## Slide 23
Art. 2416
Art. 2406

## Slide 24
Borg 6153
DALI2 and Zhaga-D4i Sensor Ready
power 53W
luminous flux 6730lm
transparent or satin
diffuser
ULOR 0%
- IP65
- IK08
- efficiency 127lm/W
- power factor PF 0,98
- ULOR 0%
- colour temp. 3000K/4000K

## Slide 25
Ø60mm standard mount
Zhaga-D4i Sensor Ready

## Slide 27
mounted on 3004 pole

## Slide 28
Hammerfest 6146
- IP65
- IK07
- efficiency 123lm/W
- driver durability 100 000h
- ULOR 1%
DALI2 and
Zhaga-D4i Sensor Ready
transparent
or opal
diffuser
ULOR 1%
Ø60mm standard mount

## Slide 29
Zhaga-D4i Sensor Ready

## Slide 30
mounted on 3004 pole
Notes: Zamocowane na słupie 300X

## Slide 31
colour temp. 3000K/4000K
PMMA diffuser
- IP65
- wattage 23.7W
- luminous flux 2239lm
- efficiency 94.5lm/W
- power factor PF>0,99
- L70B50 >72 000h
- ULOR 1%
Egersund Park 6113
Ø120mm aluminium body

## Slide 33
aluminium body
- IP65
- IK10
- wattage 12.2W
- luminous flux 1705lm
- efficiency 139.8lm/W
- colour temp. 3000K/4000K
Trysil Pole
Art. 1091
Art. 1046
durable mount
equipped with LED lens type V
(other lens versions available)

## Slide 34
Asker Head 4332
wattage 39,8W
luminous flux 5457lm
DALI2/Night Dim
- IP65
- efficiency 137lm/W
- power factor PF 0,97
- L70/B50 100 000h
- colour temp. 3000K/4000K
equipped with LED lens type II/III
(other lens versions available)
Ø60mm mount

## Slide 35
Asker Head 4332
- Ø60mm standard mount
(other mount diameters possible)
- adjustable head position angles

## Slide 36
Mora 6460
- IP65
- IK08
- wattage 17.6W
- luminous flux 1626lm
- efficiency 92.4 lm/W
- power factor PF 0,93
- L70B50 >110 000h
colour temp. 3000K/4000K
aluminium reflector
safety glass
Ø60mm mount
(other mount options possible)

## Slide 37
Mora 6467
Ø60mm mount
(other mount options possible)
colour temp. 3000K/4000K
aluminium reflector
safety glass
DALI2/NightDim
- IP65
- IK08
- wattage 33.5W
- luminous flux 3437lm
- efficiency 102.6 lm/W
- power factor PF 0,99
- L70B50 >110 000h

## Slide 38
Nidaros
- IP65
- wattage 7.8W
- luminous flux 765lm
- efficiency 98,1 lm/W
- power factor PF 0,90
- L70/B50 >110 000h
dimmable (TRIAC)
safety glass
aluminium reflector
Art. 2122
Art. 2121
Art. 2120
3 sizes (9, 18 and 23cm)

## Slide 39
Sol 4056
- IP65
- IK10
- wattage 19,1W
- luminous flux 2421lm - efficiency 126,8lm/W
- L70/B50 >100 000h
- power factor PF 0,96
transparent PC diffuser for IK10
(glass version possible, lower IK)
colour temp. 3000K/4000K
aluminium reflector
light control DALI

## Slide 40
- own tooling shop
- own die cast foundry
- own hot dip galvanizing facility
- own paint shop
- own metal workshop (classic one)
- own CNC mill departments
- own welding department
Bespoke projects
custom made die cast moulds
custom made press tools
custom made/modified steel and aluminium lantern elements
colour/finish customization
properties customization (IP, IK…)
(and modifications)

## Slide 41
- own tooling shop
- own die cast foundry
- own hot dip galvanizing facility
- own paint shop
- own metal workshop (classic one)
- own CNC mill departments
- own welding department
Bespoke projects
custom made die cast moulds
custom made press tools
custom made/modified steel and aluminium lantern elements
colour/finish customization
properties customization (IP, IK…)
(and modifications)

## Slide 42
Thank You